Instruction set for IN18 Nixie clock

Note: if your clock has battery backup, in order to start from this point you should:
1) unplug the cord
2)unplug the battery
3) plug cord back in
4) plug battery back in

When plugged in, the blue led should light immediately and the display will read 00:00:00 for five seconds.

To enable the calendar to display, press either fast set or slow set once, and the display will change to 11:11:11 for three seconds. This means the calendar has been enabled.

Then tubes should then display 1:11 for three seconds for 60HZ, or 0:00 for 50HZ. If the wrong frequency was erroneously detected, unplug, wait until the blue led goes off, and then plug back in.

Next the tubes should display: 12 (12 hour format, the default setting) for three seconds. To choose 24 hour format, press the fast set button once, and the display will change to: 24. To select 12 hour format with leading zero, press fast set again and the display will change to: 02. To select 24 hour format with leading zero, press fast set again and the display will change to: 04.  At anytime, if slow set is pressed, it will enter the main loop of normal timekeeping in the selected mode. Also, if no button is pressed for 3-5 seconds, it will enter the main loop of normal timekeeping in the selected mode, set buttons operate as fast set / slow set, (hours / minutes).

To set the calendar date: Press and hold fast set, then press and also hold the toggle button (button in the back) at the same time, and the date will fast set. Release the toggle button, but hold the fast set, and the date will display until fast set is released. Next hold down slow set & toggle to slow set the date. Again, release toggle while still holding down slow set and the date will display until slow set is released. The date should appear on the second’s count of 50 to 53. It is in mm/dd/yy format. Please refer to the youtube for illustration: youtube demo

To manually turn the display on/off , push the button in the back ( toggle )and hold for no longer than one second until the display toggles.

To program the preset on/off times from normal time keeping mode: Press both buttons and the display will blank. Press the fast set button to increment hours to the desired on time ( : 1 after the hour indicates AM , : 0 indicates PM ) .Press slow set to confirm your choice , and the hour you selected will appear with :00 for PM , :11 for AM. To set the alarm for this time, press fast set again, and “1” will be displayed on the last nixie. (xx:xx:x1 ) Please refer to youtube for illustration: alarm demo

Press either button once to enter the OFF time set mode. Follow the same procedure, and after the OFF time is confirmed (: XX appears after the hour selected), press slow set button to enter normal timekeeping (fast set, slow set) mode. To program a second set of sleep / wake times, press fast set and repeat the procedure for a second time. Please refer to the youtube link for illustration: 2nd on/off times setup demo

Note : The clock will display 12:00 AM to start (1:00 AM if in 24HR mode) so if the present time is after noon, you will need to advance the time past 12:00 in order to reach the PM hours (if in 12 HR mode) else the preset on/off times may be reversed. I.E.: if the present time is 8:00 PM, you need to advance PAST 8:00 once, then stop at 8:00.

To change the color of the led underlighting, press the ledcolor button until the color changes. If the button is held, it will cycle through all the color choices until it returns to blue (default color).

Thanks again for your purchase !